## Slide 1
Backcalculation Tool (BcT) Update
PMED User Group Meeting
Notes: Opening slide prior to the webinar starting.

## Slide 2: PMED User Group Meeting Backcalculation Tool Update September 7, 2023 3:15pm – 3:45pm

## Slide 3: Backcalculation Tool Update
Introduction
FY 2023 Enhancements
  Integrating the BcT into a Multi-Tenant Web Application
  Adding Pavement Temperature Calculation Feature
Summary
Questions

## Slide 4: Introduction
Multi-Tenant Web Application:
  AASHTOWare is in the process of converting all their products to web applications for better integration with other products and maintenance over time.
Pavement Temperature:
  Pavement temperature is needed to determine the fatigue damage index from the backcalculated elastic layer modulus for the asphalt layers.
  Measuring pavement temperatures take time and not routinely measured during FWD testing.
  Many users of the BcT requested an enhancement to calculate pavement temperature in support of FWD testing.

## Slide 5: Introduction
How to get access to the BcT web app version:
Purchased the BcT standalone license/subscription, same as for the desktop version.
Comes included with a PMED license/subscription.

## Slide 6: Introduction
Getting to the BcT – with a PMED license.
https://pavementmedesign.com
https://pavementmedesign.com/MEDesignBcT/Project

## Slide 7: BcT Multi-Tenant Web App
User Interface is different but the operation is the same to the desktop application, with the exception of the newly implemented features specific to the web-application.

## Slide 8: BcT Multi-Tenant Web App
Create new BcT analysis project from FWD file
Upload existing BcT analysis project

## Slide 9: BcT Multi-Tenant Web App
Guided process remains the same

## Slide 10: Pavement Temperature Calculation Feature
Air and Surface temperature is typically available while mid-depth pavement temperature is not
Mid-depth pavement temperature is needed to determine the fatigue damage index from the backcalculated elastic layer modulus for the asphalt layers.
Many users of the BcT requested an enhancement to calculate pavement temperature in support of FWD testing.

## Slide 11: Pavement Temperature Calculation Feature
?

## Slide 12: Pavement Temperature Calculation Feature
Two methods integrated into the BcT to calculate mid-depth temperature of asphalt layers:
Bells3 Method
Southgate/Asphalt Institute Method (Included in EverCalc)
One versus two asphalt layers used in the backcalculation process.

## Slide 13: Pavement Temperature Calculation Feature
Bells3 Method requires:
  Asphalt layer thickness.
  Previous day average air temperature.
  Start time of deflection testing.
Southgate/Asphalt Institute Method
  Asphalt layer thickness.
  Previous 5-day average air temperature during testing.

## Slide 14: Pavement Temperature Calculation Feature
Southgate/Asphalt Institute Method

## Slide 15: Pavement Temperature Calculation Feature
Bells3 Method

## Slide 16: Pavement Temperature Calculation Feature

## Slide 17: Pavement Temperature Calculation Feature
Pavement temperature is important to quantify the in place structural fatigue damage of the asphalt layers from the FWD deflection basins – the damaged dynamic modulus master curve.

## Slide 18: Pavement Temperature Calculation Feature
Multiple asphalt layers included in the pavement structure simulation.
Pavement temperature must be measured at different depths for determining the asphalt layer damaged master curve before deflection basin data measured or completed.
Pavement temperature calculated for each asphalt layer simulated in the BcT.

## Slide 19
Pavement Temperature Calculation Feature
28.4
21.7
Air temp. during FWD testing: 44 to 53 ⁰F
Calculated Bells3 pavement temp.
Previous day avg. air temp.: 48⁰F

## Slide 20: Pavement Temperature Calculation Feature
Calculated Southgate/AI pavement temp.
Air temp. during FWD testing: 44 to 53 ⁰F
Previous 5-day avg. air temp. 51 ⁰F
56.7
57.0

## Slide 21: Summary
Pavement temperature is important to quantify the in place structural fatigue damage of the asphalt layers from the FWD deflection basins – the damaged dynamic modulus master curve.
Bells3 and Southgate/Asphalt Institute methods were implemented to calculate pavement temperature but result in different values.

## Slide 22: QUESTIONS?